## Slide 1: BUILDING STONES
A Natural material of construction which is obtained from by suitable method is called a stone. The stone which is used for the construction of engineering structures is known as building stones.
Stones are derived from rocks. Rocks is a mixture of two or more minerals which forms the earth crust of earth and has no definite shape or chemical composition and is not homogenous stone.

## Slide 2: CLASSIFICATION OF ROCKS
GEOLOGICAL CHEMICAL PHYSICAL
1. IGNEOUS 1. SILICEOUS 1. STRATIFIED
2. SEDIMENTARY 2. ARGILLACEOUS 2. UNSTRATIFIED
3. METAMORPHIC 3. CALCAREOUS 3. FOLIATED

## Slide 3: QUALITIES OF A GOOD BUILDING STONE
CRUSHING STRENGTH
APPEARANCE
DURABILITY
HARDNESS , TOUGHNESS
TEXTURE
WORKABILITY
SEASONING
POROSITY
SPECIFIC GRAVITY

## Slide 4: TESTING OF STONES
CRUSHING STRENGTH TEST
HARDNESS TEST
ATTRITION TEST
WATER ABSORPTION TEST
SPECIFIC GRAVITY TEST
DURABILITY TEST

## Slide 5: STONE QUARRYING
The process of taking out stones
from natural rock beds is known as
quarrying.
METHODS OF QUARRYING
Quarrying with hand tools.
Quarrying with channelling machine.
Quarrying by blasting.

## Slide 6: DRESSING OF STONES
The stones after being quarried are to
be cut into suitable sizes and with
suitable surfaces. This process is known
as dressing of stones.

## Slide 7: GENERAL CHARACTERISTICS OF STONES
MARBLE
Its specific gravity is 2.72.
Its water absorption is 1- 3%.
GRANITE
Its specific gravity is 2.6 – 2.8.
Water absorption is hardly 0.5%.

## Slide 8
3. SAND STONE
Its specific gravity is 2.3 – 2.4.
Its water absorption is 5 – 6%.
4. TRAP AND BASALT STONE
Its specific gravity is 2.9 – 2.96.
Its water absorption is less than 0.5%.

## Slide 9
5. LIME STONE
Its specific gravity is 2.5 – 2.6.
Its water absorption is upto 4%.
6. SLATE
Its specific gravity is 2.89.
Its water absorption varies from 0.5 –1%.

## Slide 10: BRICKS
The artificial material construction in
the form of clay blocks of uniform size
and shape are known as brick.
INGREDIENTS OF GOOD BRICK
EARTH
ALUMINA OR CLAY – 20% - 30% by Weight.
SILICA OR SAND – 35 – 50% by weight.
SILT – 20 – 35% by weight

## Slide 11: MANUFACTURING OF BRICKS
The following operation are involved in the
process of manufacture of bricks.
Selection of clay
Preparation of clay
Moulding of bricks
Drying of bricks
Burning of bricks

## Slide 12: CHARACTERISTICS OF GOOD BRICKS
APPEARANCE
STRENGTH
HARDNESS
SOUNDNESS
STRUCTURE
DURABILITY
POROSITY
EFFLORESCENCE

## Slide 13: SIZE OF STANDARD BRICKS
According to IS : 1077-1970
Standard size of the brick - 190mm x
90mm x 90mm.
Nominal size of brick – 200mm x
100mm x 100mm .

## Slide 14: CLASSIFICATION OF BRICKS EARTH
LOAMY MILD OR SANDY CLAY
MARLS, OR CALCAREOUS ROCKS
PLASTICS, STRONG OR PURE CLAY

## Slide 15: THE PROCESS OF MANUFACTURE OF BRICKS
SELECTION OF CLAY
PREPARATION OF CLAY
MOULDING OF BRICKS
DRYING OF BRICKS
BURNING OF BRICKS

## Slide 16: CHARACTERISTICS OF GOOD BRICKS
APPERANCE
STRENGTH
HARDNESS
SOUNDNESS
DURABILITY
POROSITY
RESISTANCE TO FIRE
EFFLORESCENCE

## Slide 17: TESTING OF COMMON BUILDING BRICKS
DIMENSION AND TOLERANCE TEST
COMPRESSIVE STRENGTH TEST
WATER ABSORPTION TEST
EFFLORENCE TEST
SOUNDNESS TEST

## Slide 18: CEMENT
THE PRODUCT OBTAINED BY BURNING
AT VERY HIGH TEMPERATURE AND
CRUSHING TO POEWRED EITHER STONE
HAVING 20% -40% CLAY AND
REMAINING CARBONATE OF LIME OR AN
INTIMATE MIXTURE OF WELL PROPORTIONED
CALCAREOUS AND ARGILLACEOUS MATERIALS
IS CALLED CEMENT

## Slide 19: USES OF CEMENT
1.Cement mortar for plaster, painting,
masonry work.
2. Construction of roads, wells, water tank, etc.
3.Construction of foundation, water tight floors, foothpath etc.
4. Making joint for drain pipe etc.

## Slide 20: CHEMICAL CONSTITUENTS OF PORTLAND CEMENT
S.NO | INGREDIENTS | APPROX. PROPORTION | COMMON PROPORTION
1. 2. 3. 4. 5. 6. 7. 8. | Lime Silica Alumina Iron oxide Calcium sulphate Magnesia Sulphur Alkalies | 60-67% 17-25% 3-8% 3-4% 3-4% 0.1-3% 1-3% 0.2-1% | 62% 22% 5% 3% 4% 2% 1% 1%
 |  | TOTAL | 100%

## Slide 21: MANUFACTURING OF ORDINARY PORTLAND CEMENT
The following is adopted for the
manufacturing of cement :
Collection of raw materials.
Mixing : crushing, grinding, proportioning and blending of raw materials to prepare.
Burning
Grinding

## Slide 22: FIELD TESTS FOR CEMENT
Following field may be carried out
As certain roughly the quality of
Cement :-
COLOUR TEST
PHYSICAL PROPERTIES
PRESENCE OF LUMPS
STRENGTH

## Slide 23: LABORATORY TEST FOR CEMENT
Following laboratory test can be
performed on cement despatching it to
Market :-
FINENESS TEST
CONSISTENCY TEST
INITIAL AND FINAL SETTING TEST
SOUNDNESS TEST
COMPRESSIVE STRENGTH TEST

## Slide 24: VARIOUS TYPES OF CEMENT
ORDINARY PORTLAND CEMENT
QUICK SETTING CEMENT
HIGH ALUMINA CEMENT
BLAST FURNANCE SLAG CEMENT
WHITE CEMENT
LOW HEAT CEMENT
PORTLAND CEMENT
SUPER SULPHATE CEMENT
PORTLAND POZZOLAN CEMENT
CALCIUM CHLORIDE CEMENT

## Slide 25: ADMIXTURES
Some materials are added in cement
Mortar or cement concrete to improve
Upon the quality of mortar or concrete .
These materials are called admixtures.
THESE ADMIXTURES SERVE THE
FOLLOWING PURPOSES :-
1.To improve the workability.
2.To improve the water proofing properties of mortar or concrete.
3. To retard setting action of mortar or concrete.

## Slide 26: LIME
The product obtained by calcinating of lime stone is called lime.
SOURCES OF LIME
Limestone
Boulders
Kankar
Shells

## Slide 27: Different types of lime
1 Fat Lime
2 Hydraulic Lime
3 Poor Lime
Manufacturing of fat lime
. Collections of raw materials
. Transportation of raw materials
. Burning of lime stone
. Slaking of burnt lime

## Slide 28
Manufacturing of hydraulic lime
. Collections of kankar
. Transportation of kankar
. Collection of fuel
. Calcination of kankar
. Slaking and grinding of burnt lime.

## Slide 29: TESTING OF LIME
1 Visual Examination
2 Hydrochloric Acid Test
3 Ball Test

## Slide 30
THANK YOU